## Slide 1
Representation Learning for Robotic Pushing
OOD Generalization via Object-Centric & Causality-Aware Encoders with CEM-MPC
Paper 1 · MuJoCo Simulation · SO-101 Robot

## Slide 2
Research Question
How does the choice of state representation affect a learned dynamics model's ability to generalize to out-of-distribution (OOD) scenarios in robotic pushing?
Layout OOD
Can the model handle novel obstacle configurations (blocking, narrow passages) not seen during training?
Shape OOD
Can the model generalize to novel object shapes (L-shapes, crosses) trained only on T-shapes?
Representation Gap
Do object-centric or causality-aware encoders outperform flat state encoding under distribution shift?

## Slide 3
Method Overview
1. Reset Templates
140 templates across train / ID-test / OOD splits (T/L/cross/bar/square/cylinder)
2. MuJoCo Env
MujocoPushEnv with compound object geoms, obstacle instantiation
3. Oracle Rollout
True dynamics rollout for CEM cost evaluation (state clone/restore)
4. CEM-MPC
Cross-Entropy Method planner with strict pose-stop criterion
5. Evaluation
Success rate, pos/θ error, OOD gap analysis across 3 encoder variants
Three Encoder Variants (Learned Dynamics Models)
FlatEncoder
Raw state vector → z (Baseline)
ObjectCentricEncoder
Per-object slots → z (Structured representation)
CausalityAwareEncoder
Causal graph masking → z (Intervention-aware)

## Slide 4
Environment & Task Design
Object Shapes (6 families)
• T-shape (primary, 12mm thick) • L-shape (OOD shape test) • Cross, Bar, Square, Cylinder Compound MuJoCo geoms via ObjectShapeFactory
Layout Families (OOD)
• Open space (no obstacles) • Blocking (easy / medium / hard) • Passage (wide 9cm / medium 7cm / hard 5cm) • Edge goal Passage gap controls difficulty level
Pusher Configuration
• Vertical cylinder (finger) geometry • Radius: 10mm, Height: 28mm • Fixed z-axis pushing (planar task) • Validated: sphere pusher was unstable for lateral contact on thin objects
Success Criterion (Strict Pose Stop)
• Position error ≤ 1.5 mm • Orientation error ≤ 3.0° • BOTH must be met simultaneously • No legacy 5cm early-stop shortcut • Budget: 600 or 800 total steps

## Slide 5
Oracle-MPC Capacity Results
Phase 1: Can the planner solve the task with true dynamics? (No learned model yet)
✅ Open Space (train_sim_id)
c23_precise: mean pos = 2.70mm, θ = ~3° success_pos_1cm = 100% c25_fast: mean pos = 2.38mm success_0.5cm_5° = 100% → mm-level precision confirmed
⚠️ Obstacle Layouts (sixpack sweep)
passage_wide (9cm gap): ✅ both budgets passage_medium (7cm): ✅ strict800 only passage_hard (5cm): ❌ failed (~190mm) blocking (easy/med/hard): ❌ all failed (170–230mm final error) strict800 SPSR: 33% | strict600 SPSR: 17%
Key Findings
• Oracle-MPC achieves sub-2mm precision in open space — task is solvable
• Blocking layouts remain unsolved — obstacles block direct pushing paths
• Passage difficulty scales with gap width: 9cm > 7cm > 5cm
• More MPC budget (strict800 vs 600) helps borderline cases (passage_medium)
• 5cm early-stop was masking true capability — strict pose stop is the correct metric

## Slide 6
Validation Pipeline Status
✅ Completed (23 files PASS)
MuJoCo env scaffold (reset/step/clone/restore)
ObjectShapeFactory (6 shape families)
Oracle rollout + cost function
CEM-MPC optimizer interface
State sanity checks (140/140 templates)
Toy oracle-MPC (20/20)
MuJoCo oracle-MPC interface (5/5)
Reset template generation + schema
State normalizer interface
Three encoder variants (forward/backward)
RIGWorldModel unified interface
Strict pose-stop code fix
⚠️ In Progress / Blocked
Obstacle instantiation in MuJoCo ← #1 blocker
Strict pose-stop smoke test (code ready)
Success metric variable bug fix
Layout OOD capacity with real obstacles
Shape OOD capacity test

## Slide 7
Roadmap
NOW
NOW
Phase 1: Oracle-MPC Capacity
Open-space mm-precision ✅
Obstacle gate (blocking + passage)
Strict pose-stop validation
NEXT
NEXT
Phase 2: Data Collection
Collect sim data with Oracle-MPC
State normalizer fit on train only
Validate no split leakage
LATER
LATER
Phase 3: Model Training
Train 3 encoder variants
Same data, same hyperparams
Flat vs ObjCentric vs Causal
GOAL
GOAL
Phase 4: OOD Evaluation
Learned model + CEM-MPC
ID test → Layout OOD → Shape OOD
Quantify representation gap
Sprint history: Apr 20 (skeleton) → May 6 (MuJoCo env) → May 8 (oracle-MPC) → May 11-12 (sweeps + strict stop) → May 13 (obstacle sweeps)

## Slide 8
Tech Stack & Architecture
Simulation
MuJoCo physics engine
Compound geom objects (T/L/cross/...)
Custom MujocoPushEnv wrapper
State clone/restore for MPC rollouts
Planning
CEM-MPC (Cross-Entropy Method)
1024 samples, 96 elites, 5 iterations
Horizon: 80 steps
Strict pose-stop criterion
Models
PyTorch
3 encoder variants (Flat/ObjCentric/Causal)
DynamicsHead + SubgoalHead
RIGWorldModel unified interface
Infrastructure
Python + conda (lerobot env)
28-core parallel CEM evaluation
Modular scripts (debug/sweep/render)
Git-versioned experiment configs
Codebase Structure
src/ (envs, planners, models, metrics, data, interventions, utils) · scripts/ (debug, sweep, render, eval) · configs/ (planner, train, eval, splits) · data/ (reset templates, metadata) · runs/ (sweep results, videos, logs)

## Slide 9
Thank You
Questions & Discussion
Next milestone: Obstacle gate → Data collection → Model training